## Slide 1: COSMOS/ORBIT Tutorials (Introduction)

## Slide 2: Orbit Measurement Library (OML)
Hardware with (at least one) dedicated NIC for control/instrumentation
Experimenters measure node, network & application performance (i.e. a lot of numbers).
How to collect these numbers in real-time, in a
distributed environment like ORBIT?
OML design goal: distributed software infrastructure to collect measurements in real-time while providing flexible (and dynamic) way to modify the collection process.

## Slide 3: Orbit Measurement Library (OML) (2)
Push based architecture
All experiment data in one place – including metadata
Separation of concerns
  Instrumentation
  Collection
Minimize collection overhead
  Application CPU time
  Experimental traffic interference
Proxy server for disconnected operation

## Slide 4: OML Client + Server
Application or Service
Measurement
points
Filters
Measurement
streams
OML Server
Database
(SQL)
Database tables
File
OML client library
Notes: Application writer instruments application by defining measurement points
* MP’s accept typed tuples
OML client library provides filtering
* Application user configures the collection process
* what filters, what destination
Each measurement stream can be sent to different destination
Database table schemas are created dynamically
* low overhead for admin/user

## Slide 5: OML – Measurement Collection
OML Server
Application
Experiment Node
OML Server
Application
Experiment Node
Application
Experiment Node
Application
Measurements

## Slide 6: Experimental Support
Applications
Traffic Generation/Measurements
  OTG … Traffic Generator
  Iperf
Monitoring
  Libtrace
  Libsigar
  Spectrum Analyzer
  GPS
  (Weather)
Components
  TinyOS/Motes
  (GnuRadio)
Filters
Plug-in Architecture
User extensibility
Current List
Stddev
Average
First
Histogram

## Slide 7: OML2 Functions
omlc_init() – used for OML initialization
    omlc_init(arg(0), &argc, argv, o_log);
oml_add_mp() – called to register each measurement point with the container
    oml_mp = omlc_add_mp("udp_out", oml_def);
omlc_start() - used to start the local collection daemon
omlc_process() – used to specify the stages at which to collect the measurement points
    omlc_process(oml_mp, v);

## Slide 8: SS Tutorial

## Slide 9: COSMOS Summary
Focus on ultra high bandwidth, low latency, edge cloud
Open platform (building on ORBIT) integrating mmWave, SDR, and optical x-haul
1 sq mile densely populated area in West Harlem
Local community outreach
Research community:
  Develop future experiments, provide input
  (short term) get involved in the educational outreach
More information: http://advancewireless.org http://www.orbit-lab.org http://www.cosmos-lab.org
http://omf.orbit-lab.org http://oml-doc.orbit-lab.org